## Slide 1: New hire onboarding: warehouse safety
Harbor Logistics · Module 1 of 4 · 45 minutes · Trainer: Lena Park

## Slide 2: By the end of this session you will be able to
1
Identify the five hazard zones on the warehouse floor
2
Put on and check personal protective equipment in under two minutes
3
Follow the forklift right-of-way rules
4
Report a near miss using the app

## Slide 3: Agenda
10 min
Why safety matters
15 min
Zones and PPE
10 min
Forklift rules
10 min
Practice and quiz

## Slide 4: Why this matters
0
serious injuries in 2025. Keep it that way.
14
near misses reported last quarter
80%
of incidents involve forklifts or falling stock
Every rule in this module comes from a real event at one of our sites. We will walk through three of them.

## Slide 5: Lesson 1: the five hazard zones
Zone | Hazard | Rule
Loading dock | Reversing trucks, dock edges | Stay behind the yellow line unless spotting
Racking aisles | Falling stock, forklifts | Hard hat on; one person per aisle with a forklift
Charging bay | Battery acid, fumes | Goggles and gloves; no phones
Packing stations | Cutters, repetitive strain | Blade covers on; rotate every 2 hours
Mezzanine | Falls, dropped items | Harness clipped on beyond the rail

## Slide 6: Lesson 2: PPE check, every shift
1
Hard hat
Chin strap fastened, no cracks
2
Hi-vis vest
Zipped; reflective strips visible
3
Safety boots
Laced, toe cap intact
4
Gloves, goggles
Per zone sign
Two minutes at the start of every shift. Your supervisor spot-checks daily.

## Slide 7: Lesson 3: forklift right of way
Forklifts always have right of way in marked aisles
Make eye contact with the driver before crossing; wait for a thumbs-up
Never walk under a raised load, even an empty fork
Horn means stop and look, not hurry up
Pedestrians use the green walkways; forklifts never enter them
Numbers to remember
Max speed indoors: 8 km/h
Reverse: sound horn twice
Blind corners: stop, horn, proceed

## Slide 8: Practice: what would you do?
Scenario A
You see a pallet leaning in aisle 7 and a forklift approaching from the far end. What do you do first?
Scenario B
A colleague is on the mezzanine without a harness, 'just for a second'.
Scenario C
Your hard hat has a hairline crack but it is 10 minutes to the end of your shift.
Discuss in pairs for 3 minutes. We will share answers.

## Slide 9: Quick check
Question | Answer
Who has right of way in a marked aisle? | The forklift
How often is the PPE check done? | Every shift
Where do you report a near miss? | In the app, same day
Can you walk under an empty raised fork? | No

## Slide 10: Key takeaways
Know your zone and its rule before you start work
PPE check takes two minutes; do it every shift
Forklifts have right of way; eye contact before crossing
Report near misses the same day. Nobody gets in trouble for reporting
Next module: manual handling, Thursday 9:00, Training Room B.